## Slide 1: MBIE EAG Update
Canterbury Technical Forum
3 April 2013

## Slide 2: Overview
Residential
  Focus on consenting
  Information sheet for homeowners
Commercial
  Light commercial/ industrial buildings
Your Questions

## Slide 3: 1. Residential Focus on Consenting
The standard of consent documentation from some needs raising
  Main issue: clearly demonstrating the compliance path
Consent documents need a clear summary that highlights the key features

## Slide 4: Design Features Report
Purpose
  A concise overview of the structure and its design
    to facilitate the consenting process
    for future owners and engineers working on the property
SESOC template
Recap on the basic elements
  Description
  Geotechnical investigation and results
  Structural design
  Recommended Construction Monitoring

## Slide 5: Design Features Report
Description
  No. of storeys; area; roof and cladding weights; floor construction; foundation system and structural system
  Basis of design and compliance – the Verification Methods, Acceptable Solutions and Guidance followed (including any areas of departure from Guidance)
  Ground floor level (incl. flood risk requirements, where applicable)
  Technical Category (designated and confirmed)

## Slide 6: Design Features Report
Geotechnical Investigation and Results
  Investigation methods, and other data drawn upon
  Soil profile, including basic foundation bearing capacities, groundwater levels and subsoil class
  Global Lateral Movement and/ or Stretch at SLS and ULS
  Vertical Land Settlement at SLS and ULS
Structural Design
  Key loadings: seismic, wind, snow, floor loadings
  Lateral resistance
  Other design assumptions
4. Recommended Construction Monitoring
  Critical elements and stages to be inspected during construction

## Slide 7: Focus on Consenting (2)
Guidance on the use of RBW Certificates of Work, Producer Statements and Design Features Reports
  When is a CoW required?
  When are Producer Statements useful?
  Suggested engineering sign-off statements
  Including worked examples of CoWs for TC1, TC2 and TC3

## Slide 8: Information Sheet for Homeowners
IPENZ/ ACENZ/ MBIE information sheet for engineers to give to homeowners
  Managing homeowner expectations
  To communicate to homeowners the scope and limitations of engineering involvement and output
  To highlight the range of future possible performance outcomes
  To accompany engineering reports and consent documentation

## Slide 9: 2. Commercial Light Commercial/ Industrial Buildings
Currently: DEE Appendix 5A May 2012
Next: Updating and taking this guidance further
Focus: Guidance on determining ‘accept/ repair /replace’ that maintains or achieves regulatory compliance
  Decoupling and de-emphasising insurance aspects
Looking at potential vulnerabilities and consequences
  Life safety, durability, amenity aspects

## Slide 10: 3. Your Questions