## Slide 1: Canterbury Technical Forum 10 September 2013
Mike Stannard

## Slide 2
Residential guidance updates:
MBIE has released a 2nd issue of technical clarifications and updates to the guidance ‘Repairing and rebuilding houses affected by the Canterbury earthquakes’, December 2012
See http://www.dbh.govt.nz/guidance-on-repairs-after-earthquake
Topics include – structural regularity; additions to houses; garages; static bearing issues for foundations; depth of ground improvement required for TC3 foundations; foundations required for 2-storey houses; cement stabilised strength requirements; soil testing criteria; lateral spread and pile design; and surface structure details for flood areas.

## Slide 3
Regular structural plan shapes in TC3
Supplementary guidance for house foot-print design in TC3
See http://www.dbh.govt.nz/guidance-on-repairs-after-earthquake
Guidance ensures that the structural intentions of the criteria in Part C, section 11.2 Design principles, item 4 of the MBIE guidance are not compromised in practice
At designers request guidance now permits an increase in permissible aspect ratio to no greater than 3:1; together with more detailed options for ‘regular structural plan shape’. Options that extend beyond this will require specific engineering design – this is an amendment to existing guidance
9 new criteria on – application of regularity to site ground improvement; permitted rectangular base plan aspect; major and minor projections; and cut-outs
Type 1 surface structures have a maximum plan area of 150m2

## Slide 4
Regular structural plan shapes in TC3

## Slide 5
Pile design options for shallow depths of liquefaction
Supplementary guidance providing a simplified procedure for assessing kinematic pile strains
See http://www.dbh.govt.nz/guidance-on-repairs-after-earthquake
Purpose – to enable a simplified analysis of lateral spreading and kinematic interactions to check the suitability of deep pile solutions for houses in TC3
Provides guidance beyond pile type and ground conditions covered by Table 15.3 in Part C of the MBIE Guidance
Is a simplification of the pseudo-static analysis procedure for piles subject to lateral spreading proposed by Cubrinovski et al (2009)

## Slide 6: Canterbury Earthquakes Royal Commission
189 recommendations
MBIE is responsible for 177
Many involve changes to the law
Several involve significant research
Overall a five year+ timeframe
Multiple stakeholders involved

## Slide 7
Notes: MBIE’s Building System Performance Branch has drawn this together into a significant programme of work to strengthen building performance nationwide.
Mission: Learning from the Canterbury Earthquakes to strengthen national building performance
Vision: A system that people are confident delivers building that are safe in and after a disaster

## Slide 8
8
Notes: 8

## Slide 10
10
Notes: More about Standards that are referenced by the supporting documents later

## Slide 12
12

## Slide 14
14

## Slide 15
Notes: Aligning with the Natural Hazards Platform

## Slide 16
Universities: Canterbury, Auckland, British Columbia Practitioners, Quake Centre, CCANZ, MBIE
Facilitate collaboration between researchers and leverage international research
Agreement to progress four priority research work streams
  Relationships between materials characteristics, ageing and strain rates and sequence of loading
  Walls
  Diaphragms
  Effects of torsion
Also to be addressed:
  Connectivity of components and robustness of load paths
  Vertical acceleration
Recent Research Workshop on Reinforced Concrete